## Slide 2: UncertainSea - project outline
UKCP18 sea level projections Still Water Return Level (2020-2100)
EA Extreme Sea Levels (2017) Using the Mumbles tidal gauge
Visualise uncertainties in future ESL GIS, 3D rendering
Time horizons: Local government planning epoch end date (2025, 2055, 2100)
Case Study location: Swansea

## Slide 3: Sources of Uncertainty
Extreme Sea Levels at defined return periods
5th, 50th, 95th percentiles  uncertainty from downscaling, ice melt
2.5th 50th, 97.5th percentiles  uncertainty in skew surge joint probability statistics
Risk projected to future climate RCP 2.6, RCP 4.5, RCP 8.5
Present risk of coastal flooding
Future risk of coastal flooding

## Slide 4
What visuals will be most applicable to stakeholders?
What else can we consider?
  Difference in exposure impacted for high percentiles versus low?
  How might exposure change in the future?
  Future flood defences?
  Impact of coastal erosion, and its uncertainty (how significant is erosion for Swansea w.r.t other factors)?

## Slide 5: Caveats / Assumptions

## Slide 6
Note 2: Extreme sea level values are for still water sea levels only ESL values include the effects of storm surge and astronomical tides but do not specifically account for any localised increase in sea level that may be induced by onshore wave action, orientation or topography. Two additional effects are of note and can be significant in certain circumstances. Wave set-up is an increase in water level due to on shore wave action (wave setdown is the opposite). Wind set-up is where the local wind shear stress pushes the water level up at the shore (and again set-down is the opposite). Depending on the circumstances these may or may not be well accounted for in the ESL estimates. Tide gauges can be exposed to these effects or sheltered from it.
Note 9: Confidence intervals The confidence levels presented in this report and in the shapefile of 2km return levels (CFB_Extreme_Sea_Levels_2018.shp or CFB_Extreme_Sea_Levels_Estuary_2018.shp in estuaries) take account of the uncertainty associated with the skew surge joint probability statistics only. Uncertainty relating to the accuracy of the CS3X model interpolation, 2km interpolation and tidal prediction is not included. Additional uncertainty due to model inaccuracies should be considered for points labelled ‘ESTUARY_’, which were derived using local models.
Skew surge joint probability method (SSJPM)  Central to this class of statistical models is the assumption that meteorological processes are independent of tidal processes, and so any surge can occur on any tide.
Notes: 51.546477, -4.020404